## Slide 1
2024年5月13日
汇报人：张玉洁
ISL-based Multi-Satellite Collaborative
Computation Offloading and Resource Allocation in ISTN

## Slide 2
CONTENT
01
Research Motivation
02
System Model
03
MSCCORA-TD3 Algorithm
04
Performance Evaluation
2

## Slide 3
PART 1
Research Motivation
3

## Slide 4
1.1
Research Background
In "The 14th Five-Year Plan for Economic and Social Development of the People's Republic of China and the Long-Range Objectives Through the Year 2035," it is explicitly stated that "we must build high-speed, ubiquitous, integrated, interconnected, secure, and efficient information infrastructure that integrates space and earth."
LEO satellite network possesses several distinct advantages, such as low propagation delay, reduced link loss, and broad coverage areas.
ISTNs is the future trend of development
  LEO satellite network can achieve seamless coverage
  ISTNs is a national strategic need
Starlink LEO satellite constellation
LEO satellite network is anticipated to integrate with terrestrial networks, facilitating seamless coverage across all regions.

## Slide 5
1.1
Research Background
The OEC paradigm extends the computing platform to LEO satellite networks, providing computational support for ground users
MEC architecture
MEC paradigm effectively reduces service latency and enhances data processing speeds by deploying computational resources and services at the network edge.
MEC alleviates the load on traditional central cloud centers, optimizes network bandwidth utilization, reduces energy consumption, and improves the overall network efficiency.
  MEC paradigm
  ISTNs equipped with satellite edge servers
Incorporating the OEC paradigm ISTNs can simultaneously address the emerging demands for coverage and computational power. This enables seamless, low-latency computing services with global coverage for terrestrial users.

## Slide 6
1.2
Research status
High algorithmic complexity
High latency
High latency
Inability to adapt to dynamically changing network environments
Consideration of computation offloading and resource allocation issues under a single satellite scenario
Using traditional algorithms for offloading decisions and resource allocation
Using LEO satellites as a relay to expand the coverage area
Single satellite overload
Low resource utilization rate
multi-satellite collaborative computation offloading and resource allocation problem in the ISTNs
Wireless channel environment dynamically changes and tasks arrive randomly
Characterize the latency of different tasks and meet the latency constraints of the tasks
The multi-satellite collaboration leads to an increase in the dimensions of the action space and state space

## Slide 7
1.3
References
[1] S. Zhang, G. Cui, Y . Long, and W. Wang, “Joint computing and communication resource allocation for satellite communication networks with edge computing,” China Communications, vol. 18, no. 7, pp. 236– 252, 2021.
[2] Z. Song, Y . Hao, Y . Liu, and X. Sun, “Energy-efficient multiaccess edge computing for terrestrial-satellite internet of things,” IEEE Internet of Things Journal, vol. 8, no. 18, pp. 14 202–14 218, 2021.
[3] Q. Tang, Z. Fei, B. Li, and Z. Han, “Computation offloading in leo satellite networks with hybrid cloud and edge computing,” IEEE Internet of Things Journal, vol. 8, no. 11, pp. 9164–9176, 2021.
[4] X. Cao, B. Yang, Y . Shen, C. Y uen, Y . Zhang, Z. Han, H. V . Poor,and L. Hanzo, “Edge-assisted multi-layer offloading optimization of leo satellite-terrestrial integrated networks,” IEEE Journal on Selected Areas in Communications, vol. 41, no. 2, pp. 381–398, 2022.
[5] Q. Tang, Z. Fei, B. Li, H. Y u, Q. Cui, J. Zhang, and Z. Han, “Stochastic computation offloading for leo satellite edge computing networks: A learning-based approach,” IEEE Internet of Things Journal, 2023.

## Slide 8
PART 2
System Model
2

## Slide 9
2.1
Network Model
,
OFDMA
Each satellite is connected to four surrounding satellites via ISL
quasi-static model,
= {(t),(t),(t)}
virtual queue
The architecture of ISL-based collaborative OEC system

## Slide 10
2.2
Communication & Computation Model
At time slot t, the uplink data transmission rate from user j to satellite i is denoted as
Satellite-Terrestrial Communication Model:
Local Computation Model:
LEO Edge Computation Model:
During time slot t, the number of bits computed locally by user j is denoted as
During time slot t, the number of bits that can be computed at satellite k for user j is given as

## Slide 11
2.3
Queue Model
Local Computation Queue Update Model:
During time slot t , the number of task bits computed locally by user j is denoted as
After time slot t, the local computation queue is updated to
Satellite Transmission Queue Update Model:
During time slot t,the number of task bits transmitted by user j is denoted as

## Slide 12
2.3
Queue Model
After time slot t, the user sub-queue in the satellite transmission queue is updated to
Satellite Computation Queue Update Model :
During time slot t, the number of task bits computed by the satellite for user j is represented as
After time slot t, the user sub-queue in the satellite computation queue is updated to

## Slide 13
2.4
Energy Model
Local Energy Consumption Model:
In time slot t, the energy consumption for the task calculated locally by user j is represented as
Satellite Energy Consumption Model:
The transmission delay and energy consumption are denoted as
The calculated energy consumption of satellite k is expressed as
Satellite Energy Consumption Model:

## Slide 14
2.5
Problem formulation
This paper proposes an optimization problem, aiming to minimize the total energy consumption of the system to the greatest extent under the constraints of task delay and limited satellite resources. The objective function of the optimization problem is constructed as follows

## Slide 15
PART 3
MSCCORA-TD3
Algorithm
2

## Slide 16
2.1
Modeling the problem as a MDP
State Space:
Action Space:
Reward Function:
This dynamic offloading problem can be constructed as a MDP. The elements in this MDP are denoted as:

## Slide 17
2.2
Algorithm framework
TD-error
Random min-bacth sample
Environment
Experience replay buffer
Actor network
Target actor network
Loss function
Critic network
Critic network
Min
Target critic network
Target critic network
Policy Gradient Descent
TD-error1
TD-error2
Soft-Update
Random noise
Update
Update
Target policy smoothing
Update
Update

## Slide 18
PART 4
Performance
Evaluation
2

## Slide 19
4.1
The local computing capacity of each user is set to 200MHz
Evaluating System Performance with Variable Task Workloads

## Slide 20
4.2
The workload of each task is set to 400 cycles/bit
Evaluating System Performance with Variable Computing capacities

## Slide 21
QUESTIONS & ANSWERS